## Slide 1: TCOO
Charging Basics

## Slide 2: Charge Faster!

## Slide 3: Charging Standards
Level 1
  120V AC (Single Phase)
  15A Circuit – 12A Max Continuous – 1.44kW
  20A Circuit – 16A Max Continuous – 1.92kW
Level 2
  208V – 240V AC (Single Phase)
  100A Circuit – 80A Max Continuous – 19.20kW
Level 3
  Tesla CHAdeMO: 400V DC – 125A – 62.5kW
  Tesla Supercharger: 400V DC – 250kW

## Slide 4: Onboard Charger
Model 3
  Long Range 3 = 48A Max
  Short / Mid Range 3 = 32A Max
Model S/X
  Refresh 75kWh S/X = 48A Max
  Refresh 100kWh S/X = 72A Max
  Nosecone S (Single Charger) = 40A Max
  Nosecone S (Dual Charger) = 80A Max

## Slide 5: Mobile Connector (UMC)
Gen 1 -- 40A Max – 9.6kW

## Slide 6: Mobile Connector (UMC)
Gen 2 – 32A Max – 7.7kW

## Slide 7: Wall Connector (HPWC)
Gen 1 & 2 – 80A Max – 19.2kW

## Slide 8: J1772 Plug

## Slide 9: CHAdeMO Plug

## Slide 10: CCS Combo Plug

## Slide 11: J1772 Adapter

## Slide 12: CHAdeMO Adapter

## Slide 13: Things To Consider
Caution - charging too high will reduce regenerative braking.
It is normal for the cooling fans to be loud when Supercharging.
Charging will be much slower at low & high SOC.
You will lose some charge, even when plugged-in.
Use PlugShare to find charging locations.
Charging Etiquette… a topic of it’s own.

## Slide 14: Best Practices
Stay between 20% - 80%.
It’s okay to go to 10% - 90%.
Try to avoid less than 10% or more than 90%.
Charge at Level 2 if feasible.
Keep Regen at Standard.
Supercharging on trips – stay low, don’t go too high.

## Slide 15: Thanks!!